## - Technical Parameters

Max. RCF:  4980*g

Max. SPEED: 5000r/min

Max. Capacity: 32*15ml, 4x 50ml, 4x 100ml, 8x 50ml, 32x 5ml, 48x 7ml, 2×2×96Hole

Noise : ≤65dBA

Power:  AC230V 50HZ

Power consumption drive:  450W

Dimension:  465*585*462mm

Net Weight:  30KG

Time range:  0~99min

Speed accuracy:  ±50r/min

Rotors are for available for your choice.

## - Product Features

1. CE, IS09001 certification.
2. Microprocessor controlled, Programmable.
3. DC brushless motor, carbon powder pollution. 
4. Low noise. 
5. A variety of rotors, a variety of pipe support, user-selected. 
6. with electronic door locks, over speed and imbalance protection, safe and reliable. With automatic functions.
7. Digital display (LED). LED screen is shown RPM/RCF and time.
8. LED display, touch panel, automatic calculation of RCF values. 
9. Operated by programming, convenient in operation.
10. ABS using, once completed.
11. Widely used in hospital, research institutes, laboratories and other biochemical serum, plasma, and pharmaceutical products for the qualitative analysis.

## - Attachment parameters

Rotor Parameter:

| Rotor Type | Rotor No. | Capacity (ml) | Max Speed (r/min) | Max RCF (*g) | Test tube type |
| --- | --- | --- | --- | --- | --- |
| Swing-out rotor | 5001 | 4x 50ml | 5000 | 4980 | Pp round bottom Pp conical bottom |
|  | 5002 | 4x 100ml | 5000 | 4600 | Pp round bottom |
|  | 5003 | 8x 50ml | 4000 | 3040 | Pp round bottom Pp conical bottom |
|  |  | 32x 15ml 32x 5ml (adapter) | 4000 | 3040 | Pp conical bottom with lid Vacuum vessel color |
|  |  | 48x 7ml | 4000 | 3040 | Vacuum vessel color |
| Microplates rotor | 5004 | 2×2×96Hole | 3500 | 2120 | ELISA version |